## Slide 1
Current Process Idea
Fuzzy explainable condition-based maintenance for naval propulsion systems
A standard Train process for BC
  Neural network
+
  Fuzzy Classifier head
Inference
Sample
(1,14)
NN(sample)
Binary Prediction
Explainable component
Saliency gradient maps
Fuzzy Decision Tree
Root cause
Local rules
The sample predicted class 1 because (Root cause), why (local rules).
fuzzyl

## Slide 2
Explainable component example
Saliency gradient maps
For top k firing rules in the last fuzzy classifier head
Trace gradients to features
Fuzzy Decision Tree
Process for a
Sample
(1,features)
Find local samples
KNN / LIME
Train Fuzzy Decision Tree
Get local rules
Gradient saliency works with NN’s only for benchmarks
For traditional classifiers, feature importance
Rules found :
IF GT_exhaust_gas_pressure(Pexh)(bar) IS Low AND HP_turbine_exit_pressure_(P48)(bar) IS Low THEN class = 1 [support=7.12, confidence=1.00]
IF GT_exhaust_gas_pressure(Pexh)(bar) IS Low AND HP_turbine_exit_pressure_(P48)(bar) IS Medium AND GT_compressor_outlet_air_temperature(T2)(C) IS Medium THEN class = 1 [support=6.06, confidence=0.51]
IF GT_exhaust_gas_pressure(Pexh)(bar) IS Low AND HP_turbine_exit_pressure_(P48)(bar) IS Medium AND GT_compressor_outlet_air_temperature(T2)(C) IS High THEN class = 1 [support=5.66, confidence=1.00]
Feature name: GT_compressor_outlet_air_temperature(T2)(C) | Importance: 0.0182
Feature name: GT_compressor_outlet_air_pressure(P2)(bar) | Importance: 0.0126
Feature name: gas_generator_rate_of_revolutions(GGn)(rpm) | Importance: 0.0118
For top k firing rules in the last fuzzy classifier head
Trace gradients to features
Because
For top k firing rules in the last fuzzy classifier head
Trace gradients to features
e.g for, Found Anomaly
Local AUC teacher: 0.95
Trained tree with 10 nodes
Local AUC of Tree: 0.9